## Slide 1
Non-Intrusive Load Monitoring
with Harmonic Feature Fusion
and Live Learning
Modeling, Simulation and Automation of Electrical Energy Systems
TH Koeln | Soheil Ayati, Marc Steffgen
A complete laboratory NILM pipeline: one PAC4200 meter, synthetic and measured ground truth, a 17-feature RF mix model, edge-based live recognition, and training-on-the-go for unknown devices.
Why we built it
NILM estimates appliance activity from one aggregate measurement at the point of common coupling.
The practical challenge is overlap: several devices run at once, similar loads share the same P range, and PV can mask consumption by driving signed power toward zero.
The project therefore uses every measurable low-frequency signature: active/reactive power, power factor, THD, per-order harmonics and switching edges.
Loads
+ PV
PAC4200
5 Hz
NILM
who + watts?
Figure 1: Single-meter NILM objective under overlapping loads and PV-aware signed power.
Data path
Synthetic generator: eight appliance models plus baseload, PV and four-quadrant machine behavior; exact per-sample ground truth.
Aggregator: phase-wise P/Q summation, synthesized voltage/frequency, and complex vector summation of current harmonics (orders 2-40).
PAC4200 reader: persistent Modbus TCP acquisition, 5 Hz samples, session recorder, harmonic file-record probing and HDF5 output.
Measured scenario mixer: loops real single-device recordings with random ON/OFF schedules to create labelled multi-device training mixes.
Figure 2: Mix-model inference on a real three-device recording; stacked predicted power is compared with measured total power.
Implementation focus
Figure 3: Live dashboard: current devices, confidence, residual, per-device power and edge events.
The system is intentionally source-agnostic: after acquisition, synthetic scenarios, measured single-device recordings and semi-synthetic measured mixes enter the same loader, feature builder, training code and inference path.
17-feature RF mix model
Steady state: Ptot mean/std/min/max, Qtot mean/std, Q/P ratio and Stot mean.
Phase/context: L1-L3 active power, PF, THD_I and file-relative hour.
Edge features: Pstep_max, Qstep_at_Pstep, n_steps.
Bundle: presence classifier + power regressor; watts are gated by predicted presence before display.
Edge detection in detail
The live engine scans the last 8 s of P/Q samples and compares settled medians before and after the strongest jump.
An edge counts only above thresholds (about 8 W or 16 var), after quiet-state checks and a debounce interval.
Each edge is matched to single-device signatures in dP/dQ space; matched edges claim devices ON/OFF with exact timestamps.
Residual power is not forced into known classes: sustained unexplained power triggers the unknown-device teaching workflow.
Training-on-the-go
1. Unknown residual appears in the live dashboard.
2. User names the device and records an isolated OFF-ON-OFF sequence.
3. Measured scenarios are rebuilt automatically.
4. Mix and identify models retrain in the background and hot-reload.
5. New device vocabulary is stored in the model bundle; no code change is required.
Results and limits
0.916
Mix presence
macro-F1
1920 held-out
windows
7 families
2.9 W
Gated power
MAE
Presence-gated
watts shown in
the dashboard
0.955
Identify
macro-F1
Real active
windows
row split caveat
Figure 4: Identification confusion matrix for seven measured device families.
What worked
End-to-end loop works: record, mix, train, infer, run live, detect unknowns and retrain.
Event features improved the measured-data mix model compared with the earlier frozen bundle.
The live monitor combines RF window predictions with edge claims, so fast switching information is not lost inside 10 s windows.
What can be improved
Record real PV during actual generation; current PV recordings contain almost no generated power.
Measure several sessions per device and more variants of small fans, then use grouped evaluation by session.
Run feature ablations: common vs harmonic, 14 vs 17 aggregate features, and with/without edge features.
Use sequence models (CNN/LSTM or seq2point) for long appliance cycles such as washing machines.
Validate on true simultaneous multi-device recordings, not only semi-synthetic measured mixes.
Conclusion
A 5 Hz industrial power meter is enough for a useful NILM laboratory system when its processed channels are fused deliberately. The current implementation is not just an offline classifier: it is a deployable workflow with measured data ingestion, RF presence/power inference, edge-aware live events, residual honesty and guided learning for unknown loads.
Key implementation artifacts
Scripts/PAC4200_reader/pac_reader.py: Modbus acquisition, dashboard, HDF5 recorder.
Scripts/Aggregator/mix_measured_scenarios.py: real recordings to labelled training mixes.
Scripts/MS2_Pipeline/nilm_pipeline.py: loaders, feature extraction and 17-feature AGG_FEATURES.
Scripts/MS2_Pipeline/train.py: RF/LGBM/MLP tasks; mix bundle stores features, devices and metrics.
Scripts/MS2_Pipeline/live.py: live inference, edge claims, residual monitor and teach/retrain loop.
Evaluation protocol
Mix model: grouped held-out split over measured scenarios, ON threshold 5 W.
Metrics travel with the model bundle: feature list, appliance vocabulary, F1 and MAE.
Real mixed recordings without per-sample ground truth are evaluated as expected device sets parsed from filenames.
The poster reports tracked metrics from output/train_mix_metrics.json and output/train_identify_metrics.json.
Sources
Hart (1992) Nonintrusive appliance load monitoring; Sahoo et al. (2020) feature fusion for NILM; Siemens SENTRON PAC4200 system manual; project docs 01-09; tracked model metrics in Scripts/MS2_Pipeline/output. Figures are generated from repository artifacts and live-system screenshots.
Repository focus: reproducible synthetic corpus, measured PAC4200 recordings, semi-synthetic measured mixes, RF/LGBM/MLP training paths and Streamlit/Flask live interfaces.